University of Toronto, Faculty of Applied Science and Engineering
Department of Electrical and Computer Engineering

ECE 243S – Computer Organization – 2015
Simple Multi‐Cycle Processor
# Overview
This implementation of a simple multi‐cycle processor consists of the datapath, control (FSM), and various inputs and outputs. The processor supports only fixed‐length 8‐bit instructions and data, and can only access memory one byte at a time. Overall, 10 instructions are implemented in hardware.
# Functional Description
The inputs and outputs include:
## Inputs:
- reset – clears the values of all registers and control signals, resets the condition flags, and resets the control FSM ( KEY[0] )
- clock – all writes and cycle transitions happen on the positive edge of the clock ( KEY[1] )
- HEXsel[1..0] – selects one of the four registers to be displayed on the hex displays; this exists for the users of the DE1 board, which does not have many hex displays. The chooseHEXs circuit component can still be used to display four values simultaneously (for example, of the four registers), but that requires eight hex displays, available only on the DE2. Users of the DE2 can make the necessary circuit connections if they so desire. ( SW[17..16] )

## Outputs:
- PCWrite – LEDR[17]
- AddrSel – LEDR[16]
- MemRead – LEDR[15]
- MemWrite – LEDR[14]
- IRLoad – LEDR[13]
- OpASel – LEDR[12]
- MDRLoad – LEDR[11]
- OpABLoad – LEDR[10]
- ALU1 – LEDR[9]
- ALU2[2..0] – LEDR[8..6]
- ALUOp[2..0] – LEDR[5..3]
- ALUOutWrite – LEDR[2]
- RFWrite – LEDR[1]
- RegIn – LEDR[0]
- FlagWrite – LEDG[7]
- N (negative) – LEDG[1]
- Z (zero) – LEDG[0]
- Register Display
  - upper 4 bits HEX1[6..0]
  - lower 4 bits HEX0[6..0]
  - Note: as mentioned previously, the circuit can be modified to support the remaining 6 hex displays, available on the DE2 board.

## Instructions
- Addition (add)
- Subtraction (sub)
- NAND (nand)
- Shifting (shift)
- OR with Immediate (ori)
- Load (load)
- Store (store)
- Branch If Positive Zero (bpz)
- Branch If Zero (bz)
- Branch If Not Zero (bnz)